## Slide 1: Analyzing air quality in Stuttgart using official and Citizen-Science data
Seminar: GIS Analyses with FOSSGIS Speakers: Amandus Butzer, Julian Käflein Teacher: Christina Ludwig 29.01.2019

## Slide 2: Motivation
Source: https://www.stuttgart.de/feinstaubalarm/
https://www.dw.com/en/stuttgart-germanys-beijing-for-air-pollution/a-18991064

## Slide 3: Motivation
Source: https://luftdaten.info/en/home-en/

## Slide 4: Motivation
Particulate Matter (PM) Defintion: Solid and liquid airborne particles under 10/2.5µm diameter (PM10/PM25)
  Health hazards: Short term irritation/ inflammation of respiratory system, allergic reactions, asthma
  Long-term increase of cardiovascular, respiratory diseases
  Sources: Industrial processes, Heating, Traffic
Stuttgart:
  Problem (1): Concentration of PM exceeding German/ European limits in recent
  Reaction: Introduction of „Feinstaubalarm“ – plea to use public transport, ban of ‚comfort heating‘
  Problem (2): Amount of PM sensors – 3 sensors by Landesanstalt für Umwelt Baden-Württemberg (LUBW)

## Slide 5: Scientific goal
(How) can we analyze the particulate matter concentration
  in the city of Stuttgart
  based on Volunteered Geographic Information (VGI)
  using Free and Open Source Geographic Information Systems (FOSSGIS)
  in an automated process?

## Slide 6: Research area

## Slide 7: Workflow
e
Luftdaten:
Rate: Hourly values
Sensors: All (global)
Format: JSON
URL: https://data.sensor.community/static/v2/data.1h.json
Size: ~ 9MB (!)

## Slide 8: Workflow
LUBW
Rate: Hourly values
Sensor: All (Baden-Württemberg)
Format: GeoJSON
URL: https://lupo-messwerte.appspot.com/ generic?table=bw_luft_stammdaten&limit= 999&filter=aktiv:true;type:- Spot&order=NO2-today-latest-class
Size: 228KB

## Slide 9: Workflow
e
e
Workflow
Download data every hour
Insert raw data into staging database
Parse raw data:
  3.1. LUBW: Select all Stations within Stuttgart Select relevant air quality values
  3.2 Luftdaten:
  Build geometry from Lat/Lon
  Select only relevant values / sensors
  Clip stations within Stuttgart
Insert stations / values into tables

## Slide 10: Workflow
Workflow

## Slide 11: Analysis
Daily average PM10 concentration for LUBW sensors vs Luftdaten sensors within 1000m distance
Method: Buffering, daily average comparison
Software: PostGIS, Grafana
Relevant Parameters:
LUBW PM10 sensor data
All Luftdaten sensors within 1km
    Script in GitHub repo

## Slide 12: Analysis
Daily average PM10 concentration – difference coefficient
Method: Buffering, daily coefficient comparison
Software: PostGIS, Grafana
Relevant Parameters:
LUBW PM10 sensor data
All Luftdaten sensors within 1km
    Script in GitHub repo

## Slide 13: Analysis - Interpolation
12µg/m³
24µg/m³

## Slide 14: Method – Inverse Distance Weighted
Interpolated Point = linear weighted combination of nearby values
Power: Defines Distance Impact on value.
No interpolation outside value range
Good for data correlated to distance (noise)

## Slide 15: Method – B-Splines
Like IDW the surface passes exactly through datapoints
„Rubber Sheet glued to points“ Minimum curvature Interpolation outside value range
Smoother surface Using Tykhonov regularization
https://upload.wikimedia.org/wikipedia/commons/thumb/f/fd/
Spline_%28PSF%29.png/220px-Spline_%28PSF%29.png
http://www.geography.hunter.cuny.edu/~jochen/GTECH361/
lectures/lecture10/3Dconcepts/Spline_files/image001.gif

## Slide 16: Method – Regularized Splines w. Tension
Tension and Smoothing of Splines possible
Plethora of output possible: - elevation(basic value output) - slope - aspect - curvatures - treeseg -> Best interpolation method so far
https://www.researchgate.net/profile/Domenico_Sguerso/publication/228701243/figure/fig12/AS:302005378666509@1449015101871/Sketch-of-RST-interpolation-results-with-high-low-tension-and-smoothing-equal-or-not-to.png

## Slide 17: Method – Reclassification
EU-defined Common Air Quality Index (CAQI)
Using Background Index as station position not exact enough. Method: r.reclass
http://www.airqualitynow.eu/about_indices_definition.php

## Slide 18: Method – Advanced Raster to GeoJson
r.to.vect
v.generalize
v.out.ogr
categorized raster
category polygons in geojson

## Slide 19: Analysis – Milestones so far
Automated download of data
Automated ingestion of data into database
Automated parsing and filtering of extreme values
Connection of GRASS GIS modules to database
Import of stations and data
Automated interpolation of air quality data to raster
Routing WebApp to avoid highly polluted areas

## Slide 20: Results
Method: IDW-Interpolation
Software: GRASS-GIS
Module: v.surf.idw
Relevant Parameters:
input: luftdaten_pm10_latest
power (factor): 2.0
npoints=12

## Slide 21: Results
Method: B-Spline-Interpolation
Software: GRASS-GIS
Module: v.surf.bspline
Relevant Parameters:
input: luftdaten_pm10_latest
lambda_i=0.01
ns_step=50
ew_step=50

## Slide 22: Limitations of the analysis
Method: RST-Interpolation
Software: GRASS-GIS
Module: v.surf.idw
Relevant Parameters:
input: luftdaten_pm10_latest
tension=40
smooth=0.5
segmax=10
npmin=50

## Slide 23: Routing Webapp
Vue webapp using
- vue2leaflet
- openrouteservice-js
- category geojson as avoid polygons

## Slide 24: Results
Modelling air quality / pollution in Stuttgart
Official sensors
  Sparse network of official sensors in research area
  Modelling air pollution impossible without additional information
Luftdaten.info sensors
  Relatively large, non-systematic discrepancy between Luftdaten and LUBW sensors (cf. LUBW 2017)
  BUT
  Luftdaten network can sense general particulate matter trend in Stuttgart
  SO
  Citizen Science / Volunteered Geographic Information enriches model

## Slide 25: Limitations of the analysis
Accuracy of Luftdaten sensors
  Need to filter extreme values (both absolute and relative)
  Constant discrepancy to official measurements
Interpolation parameters are „best fit“
  No ‚correct‘ solution to model pollution rasters from sensors
Small scale of study area
  Large effects of additional factors, i.e atmospheric conditions (wind / precipitation) /
  land cover (buildings / parks)
  Short amount of sensing time so far

## Slide 26: Limitations of the analysis
Method: RST-Interpolation
Software: GRASS-GIS
Module: v.surf.rst
Relevant Parameters:
input: luftdaten_pm10_latest
power (factor): 2.0
npoints=12

## Slide 27: Recommended literature
Briggs, D. et al. (1997) Mapping urban air pollution using GIS: a regression-based approach, International Journal of Geographical Information Science, 11 (7), 699-718.
Li, L. Zhou, W. Tong, W. (2019): Spatiotemporal Analysis of Air Pollution and Its Application in Public Health. Amsterdam, Oxford, Cambridge: Elsevier. 328 p.
LUBW (2017): Messungen mit dem Feinstaubsensor SDS01. Ein Vergleich mit einem eignungsgeprüften Feinstaubanalysator. Online source: https://pudi.lubw.de/detailseite/-/publication/90536-Ein_Vergleich_mit_einem_eignungsgepr%C3%BCften_Feinstaubanalysator.pdf
Matějíček et al. (2006): A GIS-based approach to spatio-temporal analysis of environmental pollution in urban areas: A case study of Prague's environment extended by LIDAR data. In: Ecological Modelling. 199 (3), 261-277.